## Slide 1
Lab Book 1.0. Waveguides
Student:

## Slide 2: Instructions General
SCRIPTS
From GitHub 
  Fork the repo: https://github.com/cccanvas-upv/cifoin-lab1.git
  Clone the repo using VSCode
Run the Jupyter Notebook:
  WAVEGUIDES_Student.ipynb
h
(height)
W (width)
Core
Cladding
W (width)
Core
Cladding
Slab
h_slab
h_core
shallow waveguide
deep waveguide

## Slide 3: Learning outcome #1 – Effective index of a waveguide
INSTRUCTOR:
Present Python and GDSFactory: materials, output, results.
Explain how to run a simulation for a particular cross-section.
Showcase how to change between shallow and deep waveguide.
Describe how to change the wavelength and width for the waveguide analysis.
Describe the outputs.
ALL EXAMPLE #1: waveguide width 1.2 µm, deep wvg, wavelength start and end same 1.55 µm  all ”Run”
ALL: Follow instructor, that will show how to 1) plot mode, 2) explore the results (neff …)
The differences in the refractive indices of silicon, SiO2, and silicon nitride are significant, but in all cases, the relationship between n and wavelength is nonlinear. I assume that is why they are used for different applications. I can see that for the given parameters, only the fundamental mode's field (and maybe the second mode's) is mostly confined to the core. This is related to their refractive index.

## Slide 4: Learning outcome #1 – Effective index of a waveguide

## Slide 5: Learning outcome #1 – Effective index of a waveguide
Parameters:
Effective index of each mode:
1.60524792+0.00010066j, 1.52829803+0.00017753j, 1.45072999+0.00019228j, 1.43325817+0.00021838j
Fraction_te for each mode:
0.99505426, 0.01004259, 0.96264794, 0.047651
Fraction_tm for each mode:
0.00494574, 0.98995741, 0.03735206, 0.952349

## Slide 6: Learning outcome #1 – Effective index of a waveguide

## Slide 7: Learning outcome #2 – Wavelength behavior Wavelength 1.5-1.6 µm (step 0.01 µm) – width 1.2 µm
The effective refractive index (neff) is higher in shallow waveguides than in deep waveguides, and this effect becomes more pronounced as the mode number increases. Furthermore, the decrease in neff with increasing wavelength is similar for both types of waveguides.
shallow waveguide
Paste plot here
deep waveguide
Paste plot here
slab = 150nm

## Slide 8: Learning outcome #3 – Width dependence Width 0.6 - 1.6 µm (step 0.1 µm) – Wavelength 1.55 µm
As the waveguide width increases, the phase velocity of modes 1 and 2 decreases (corresponding to an increase in neff), whereas modes 2 and 3 exhibit an increase in velocity (a decrease in neff).
deep waveguide
Paste plot here

## Slide 9: Learning outcome #4 – Waveguide compact model - Find the compact models of the following waveguides: Deep waveguide, h=300nm, w=1.2um - Shallow waveguide, core h=300nm, slab h=150 nm, w = 1.2um
Find the second-degree polynomial coefficients and relate them with the group index and the dispersion parameter.
Comment on the results found for the TE0 and TM0 for both deep and shallow waveguides.
deep waveguide
neff_TE0 vs with the second-degree polynomial fit
& neff_TM0 vs with the second-degree polynomial fit
shallow waveguide
neff_TE0 vs with the second-degree polynomial fit
& neff_TM0 vs with the second-degree polynomial fit
slab: 150nm

## Slide 10: Learning outcome #4 – Waveguide compact model - Find the compact models of the following waveguides: Deep waveguide, h=300nm, w=1.2um - Shallow waveguide, core h=300nm, slab h=150 nm, w = 1.2um
second-degree polynomial coefficients for short waveguide, D:
Quadratic fit coefficients (mod1): [ 0.0956958 -0.18817489 1.62409063]
    Quadratic fit coefficients (mod2): [ 0.14801168 -0.1325985 1.54189536]
    Ng for mode 1: 1.9157617116968038
    Ng for mode 2: 1.7474230444068224
    D for mode 1: -989.5411991849512 ps/(km*nm)
    D for mode 2: -1530.5127982607453 ps/(km*nm)
second-degree polynomial coefficients for deep waveguide, D:
Quadratic fit coefficients (mod1): [ 0.09735507 -0.21617695 1.60491663]
    Quadratic fit coefficients (mod2): [ 0.15383171 -0.15795878 1.52718923]
    Ng for mode 1: 1.939990900810061
    Ng for mode 2: 1.7720253478666539
    D for mode 1: -1006.6987866653995 ps/(km*nm)
    D for mode 2: -1590.694823439326 ps/(km*nm)
Deep waveguides are better at keeping the light in.

## Slide 11: Learning outcome #5 – Bend waveguide radius vs. loss – deep Find neff_TE0 for wvl 1.55 µm, width 1.2 µm for R=25,50,75,100, 125,150 µm
Comment results, which is the safe radius?, consider safe means less than 0.1 dB/90º.
Safe radius is under ~25um.
deep waveguide
Paste Total Loss (dB/90º) vs R & neff_TE0 vs R

## Slide 12: EXTRA 1
Neff is much higher for Si especialy for low-n modes.
deep waveguide
Paste Total Loss (dB/90º) vs R & neff_TE0 vs R

## Slide 13: EXTRA 2
The neff is significantly (too high) higher for silicon (Si), and the curvature of the effective index plots exhibits a more logarithmic character. There is probably a comutational error.
deep waveguide
Paste Total Loss (dB/90º) vs R & neff_TE0 vs R

## Slide 14: EXTRA 3
The safe bending radius is extremely small but increases rapidly with changing radius.
deep waveguide
Paste Total Loss (dB/90º) vs R & neff_TE0 vs R

## Slide 15: Thank you